## Slide 1: Implementing integrated machine learning strategies to accelerate high accuracy fracture growth simulators
John Walding
Supervisor: Dr. Adriana Paluszny Rodriguez

## Slide 2: Agenda
Motivation
Introduction
Background: SIF
Problem Specification
Implementation
Testing Strategy
Results
Conclusion
Future Developments

## Slide 3: Motivation
Fracture Simulation is of great importance to many fields
  Hydraulic Fracturing
  Mineral Extraction
  Medical Osteology
FDEMs are very accurate but can be slow
Is it possible to improve time efficiency without loss of accuracy?

## Slide 4: Introduction
ML has been applied to fracture problems before
Can be effective for certain criteria
Often limited by:
  Restricted dimensionality
  Graph theoretic approach
Not currently applicable to real world problems
Source: (Hunter, et al., 2019)

## Slide 5: Introduction
Avoid aforementioned limitations by accelerating an FDEM
Calculation of SIF required before fracture tip evolution
SIF computation requires solution of several PDEs – computationally complex
Fracture tip evolution is well understood and simple by comparison
Is it possible to predict the SIF without the preceding computation?

## Slide 6: Background: SIF
Most important quantity for this project is Stress Intensity Factor (SIF)
The SIF is a theoretical construct that encodes the stress state at a tip
SIF has three elements:
  - opening damage – positive definite
  - in-plane shearing
  - out-of-plane shearing
is often dominant, and are harder to predict

## Slide 7: Problem Specification
Two factors relevant to an accelerator:
  Time efficiency
  Accuracy
For an ML method, time efficiency applies to training and execution
  Training time of diminished importance
  Execution time almost guaranteed to be superior to current algorithm
Therefore primary objective is accuracy retention

## Slide 8: Problem Specification
This is a regression problem
Fracture tip evolution is determined by the current configuration
  Therefore configuration history information is not necessary
Inter-fracture geometric data is important for interactions
Data is gathered from runs of the Imperial College Geomechanics Toolkit (ICGT)

## Slide 9: Implementation
Feed forward neural network selected
Python implementation – chosen for ML libraries
PyTorch used for the ML aspects
Little attention given to hyperparameters at this stage
Input data formatted as a CSV
Data split as 80:10:10 for training : validation : testing

## Slide 10: Testing Strategy
Testing strategy designed for hyperparameter optimisation
Optimal configuration infeasible to ascertain
Heuristic approach taken
  Hyperparameters tested in order of expected significance
  Order investigated with preliminary testing
Will not result in optimal configuration, but adequate
Hyperparameters tested are:
  Feature set
  Model architecture
  Optimiser
  Criterion function
  Activation function
Further hyperparameters left as defaults

## Slide 11: Testing Conclusions
n=1
n=25
n=200
n=100
n=50
n=1
Feature Set: position vector, orientation vector, old SIF
Architecture: see diagram
Optimiser: Adam
Criterion Function: L1Loss
Activation Function: LeakyReLU

## Slide 12: Results -

## Slide 13: Results -

## Slide 14: Results -

## Slide 15: Conclusions
ML acceleration of an FDEM is viable
easier to predict than and
Further inter-fracture geometric data must be incorporated into feature set
Outputs currently returned with insufficient accuracy for immediate practical implementation

## Slide 16: Future Developments
Increased dataset size
Improved hyperparameter optimisation scheme
Addition of fracture interaction index – see diagram
Implementation of binary measure for fracture interaction

## Slide 17: Thank you for your attention Any questions?